N312TF Flight Test Plan

First Flight:  July 7, 2009

### First Flight

- Pilot rested and ready

- Careful preflight inspection per owner’s manual complete

- Start engine per checklist

- Check oil pressure

- Set Airspeed Bug at 85MPH on Dynon

- ATIS while warming up, mark canopy stop point

- Taxi to Runway 24, runup per checklist

- If chase plane, ask it to announce intentions to HIO

- Full Power

- Check airspeed alive, oil pressure, abort if ANY problems

- Stick back to pull nosewheel off the ground

- Flaps up when off the ground

- Check controls (elevator, ailerons, rudder) with small movements

- Climb at 110 – 120 MPH

- At 500’, reduce to 25” MP, 2500 RPM

- Hillsboro tower, experimental N312TF with ___,  just off Sunset Airstrip runway 24, on the first test flight in this aircraft.  Intend to orbit overhead Hillsboro at 4500’

- Climb to just west of Milnes Road, then orbit up to 4500

- Reduce to 23” mp, 2300 rpm

- Turn towards Hillsboro

- Orbit HIO clockwise (right turns) at 4500’, let tower know status. Mode C?

- Maintain 23”, 2300 RPM or better

- Check oil temp < 230F

- Check CHT < 440F

- Speak observed temps, recorded by video camera

- If chase plane present, compare airspeed

- On 2nd orbit, slow aircraft to 100 MPH

- Lower Flaps

- Perform slow flight, note indicated airspeed when aircraft gets mushy

- If chase plane present, compare airspeed

- If any serious problems, land at HIO, otherwise return for landing at Sunset per checklist

- Note any discrepancies

- Remove cowl and check for leaks

- GRIN!

### Flight 1

### Goals

- Test basic aircraft operation

- Perform slow flight and record indicated airspeed

- Check basic radio operations

- Check transponder operations

### Results

- .5 hours flown on 7/7/09  (.5 hours total time)

- Loud buzzing heard at various airspeeds and prop settings

- Aircraft controls smooth, no obvious rigging problems yet

- Headset audio good, except when PTT switch pressed

- Ground heard radio transmissions OK

- No Airspeed indication, either from Dynon or IK 2000 engine monitor

- No Mode C per HIO tower

### Post Flight Operations

- Suspect buzzing was caused by access door from forward baggage box into instrument bay not being secured.

- Open Pitot line found … not connected to IK 2000 engine monitor

- Dynon set for Encoder type 4 instead of 3

- Cowl removed, no leaks detected

### Flight 2

### Goals

- Verify that buzzing is gone

- Verify that airspeed is displayed

- Start engine break-in period … run at 65%-75% power for 1 hour

- Monitor temperatures

### Results

- .7 hours flown on 7/10/09 (1.2 hours total time)

- Buzzing still occurs

- Airspeed indication functional on both Dynon and IK2000

- PTT use still results in noisy audio

- 3 straight-ahead stalls perforrmed

### Post Flight Operations

- Cowl removed, no leaks detected

- Chafing noted between oil cooler control cable and FADEC wires:  tubing added to protect wires.

- Noted that right exhaust pipe was very close to engine mount.  Possible source of buzz … repositioned exhaust pipe.

- Suspect bad Molex connections on PTT wires below main stick:  cut wires and wire nut for test

- About 1 quart of oil has been consumed.

### Flight 3

### Goals

- Verify that buzzing is gone

- See if PTT operations are no longer noisy

- Continue engine break-in period … run at 65%-75% power

- Monitor temperatures

### Results

- 1.3 hours flown on 7/11/09 (2.5 hours total time)

- Buzzing still present, can find a power setting where it goes away

- PTT operations seem to be better, but HIO was very busy so I didn’t do a radio check

- Oil temps held between 220 - 238

### Post Flight Operations

- Suspected buzzing might be caused by door to back of panel, or by the glove box not being connected to the forward bracket.  Added padding  between these elements

### Flight 4

### Goals

- See if  buzzing is gone or if it has changed

- Continue engine break-in period … run at 65%-75% power

- Monitor temperatures

### Results

- .7 hours flown on 7/11/09 (3.2 hours total time)

- Buzzing still present.  @&@#$!@#)($

- Oil temps held between 215 - 238

### Post Flight Operations

- Suspected buzzing might be caused by wheel pant brackets.  Added braces on both mains.

- Added tie wrap to keep heater control line away from fuselage.

- Added rubber tubing to insure that fuel line internal to cockpit does not touch bulkhead.

### Flight 5

### Goals

- See if  buzzing is gone or if it has changed

- Continue engine break-in period … run at 65%-75% power

- Monitor temperatures

### Results

- 1.5 hours flown on 7/18/09 (4.7 hours total time)

- Buzzing still present.  Seems to appear around 140 mph indicated.

### Post Flight Operations

- Suspected buzzing might be caused by pin holding canopy to rear guide rail … marks on aluminum indicate that the pin was hitting the fuse..

### Flight 6

### Goals

- See if  buzzing is gone or if it has changed

### Results

- .4 hours flown on 7/18/09 (5.1 hours total time)

- Buzzing still present.

### Post Flight Operations

- Suspected buzzing might be caused by canopy skirt vibrating against the fuselage

- Added foam insulation underneath rear portion of the skirt.

### Flight 7

### Goals

- See if  buzzing is gone or if it has changed

### Results

- 1.3 hours flown on 7/18/09 (6.4 hours total time)

- BUZZING IS GONE!

- Flew for 1 hour between 24-squared and 25-squared before refueling at Twin Oaks

### Flight 8

### Goals

- Continue engine break-in

- Aircraft instrument familiarization

### Results

- 1.8 hours flown on 7/19/09 (8.2 hours total time)

- Dynon and IK2000 capabilities explored

- Played with GPS.

### Post Flight Operations

- Checked oil, still show 7 quarts present

- Noted that cylinders 1 and 2 run cooler than 3 and 4, with #1 being significantly cooler

- Need a permanent solution for canopy buzz problem:  foam blew out on taxi

### Flight 9

### Goals

- Continue engine break-in

- Shoot some video

### Results

- 1.2 hours flown on 7/19/09 (9.4 hours total time)

- Noted significantly worse audio, got better when intercom placed in pilot only mode

### Post Flight Operations

- Checked oil, still show 7 quarts present

- Noted that passenger audio jack (used by video camera) is loose

### Flight 10

### Goals

- Continue engine break-in

- Check audio with PTT after check of passenger audio jack

- Monitor oil temp (238 degrees seen … too high!)

### Results

- 1.1 hours flown on 7/22/09 (10.5 hours total time)

- Audio still bad … loud hissing when PTT pressed

- Oil temps still high … 225 - 238

### Post Flight Operations

- Checked oil, still show 7 quarts present

- Removed line to top of oil cooler … oil is present

- Filled some small holes in the engine baffle

- Reduced size of hole to FADEC cooling tubes

- Removed oil temp sensor and checked it in water to 212 degrees … reasonably accurate

### Flight 11

### Goals

- Continue engine break-in

- See if oil temperature has been reduced

### Results

- 1.1 hours flown on 7/26/09 (11.6 hours total time)

- Oil temps still too high

### Post Flight Operations

- Checked oil, still show nearly 7 quarts present

- Emailed Mahlon Russell re:  engine break-in and oil temps:  his response is that it sounds like the engine is broken in, and I need to deal with the oil temperature.

- Noted in Lycoming engine book that I had plumbed the oil to and from the oil cooler correctly if the TMX IOF-360 is most like an IO360B.  But if it is most like an IO360A (and I can convince myself that this might be the case, based on the picture in the Lycoming book), it is plumbed backwards.  Swapped the connections to the oil cooler.

- Emailed FlightTech Intercom re:  hissing with PTT.  Their response:  adjust the gain of the Lightspeed mic downward.

- Noted some discoloration in the lower left portion of the cowl … added a heat diffuser on the exhaust stack.

### Flight 12

### Goals

- Continue engine break-in

- See if oil temperature has been reduced

### Results

- 0.6 hours flown on 7/28/09 (12.2 hours total time)

- Oil temps still too high

### Post Flight Operations

- Emailed Mahlon for ideas

- Removed vernatherm and tested in hot water.  It did not open up, even at 212 degrees.  Replacement part ordered.

### Flight 13

### Goals

- Continue engine break-in

- See if oil temperature has been reduced

### Results

### Subsequent Flights

- Engine Break-in:  run hard until oil consumption stabilizes per Mattituck recommendations for first 15 hours

- For the following, use Van’s recommendations and AC 90-89A.  Record Engine data and temps

  - Slow Flight (record Engine data, temps)

  - Stalls

  - Best Rate of Climb

  - Best Angle of Climb

  - Climb Performance Tests

  - Glide Performance Tests

  - Airspeed Calibration

  - Stability Tests

  - Fuel Consumption Tests

  - CG Loading

  - G Loading

  - Spin Testing